## Slide 1: Lecture
Scheduling

## Slide 2: Scheduling
© 2006 Prentice Hall, Inc.
Objective of Scheduling is to achieve trade offs among conflicting goals ,which includes efficient utilization of staff equipment and facilities and minimization of customer waiting time , inventories and processing time.

## Slide 3: Importance of Scheduling
Effective and efficient scheduling can be a competitive advantage
  Faster movement of goods through a facility means better use of assets and lower costs
  Good schedules result in more reliable deliveries
© 2006 Prentice Hall, Inc.

## Slide 4: Sequencing Jobs
Specifies the order in which jobs should be performed at work centers
Priority rules are used to dispatch or sequence jobs
  FCFS: First come, first served
  SPT: Shortest processing time
  EDD: Earliest due date
  LPT: Longest processing time

## Slide 5: Sequencing Example
Job | Job Work (Processing) Time (Days) | Job Due Date (Days)
A | 6 | 8
B | 2 | 6
C | 8 | 18
D | 3 | 15
E | 9 | 23
Apply the four popular sequencing rules to these five jobs in order to find:
Average Completion time (or average flow time)
Utilization
Iii. Average number of jobs in the system
iv. Average job lateness (or average tardiness)

## Slide 6: Sequencing Example
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
A | 6 | 6 | 8 | 0
B | 2 | 8 | 6 | 2
C | 8 | 16 | 18 | 0
D | 3 | 19 | 15 | 4
E | 9 | 28 | 23 | 5
 | 28 | 77 |  | 11
FCFS: Sequence A-B-C-D-E

## Slide 7: Sequencing Example
Job Work
Job (Processing) Flow Job Due Job Sequence Time Time Date Lateness
A 6 6 8 0
B 2 8 6 2
C 8 16 18 0
D 3 19 15 4
E 9 28 23 5
28 77 11
FCFS: Sequence A-B-C-D-E
Average completion time = Sum of total flow time = 77/5 = 15.4 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/77 = 36.4%
Average number of = Sum of total flow time = 77/28 = 2.75 jobs
Total job work time
Average job lateness =
= 11/5 = 2.2 days
Total late days Number of jobs

## Slide 8: Sequencing Example
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
B | 2 | 2 | 6 | 0
D | 3 | 5 | 15 | 0
A | 6 | 11 | 8 | 3
C | 8 | 19 | 18 | 1
E | 9 | 28 | 23 | 5
 | 28 | 65 |  | 9
SPT: Sequence B-D-A-C-E

## Slide 9: Sequencing Example
Job Work
Job (Processing) Flow Job Due Job Sequence Time Time Date Lateness
B 2 2 6 0
D 3 5 15 0
A 6 11 8 3
C 8 19 18 1
E 9 28 23 5
28 65 9
SPT: Sequence B-D-A-C-E
Average completion time = Sum of total flow time = 65/5 = 13 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/65 = 43.1%
Average number of = Sum of total flow time = 65/28 = 2.32 jobs
Total job work time
Average job lateness =
= 9/5 = 1.8 days
Total late days Number of jobs

## Slide 10: Sequencing Example
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
B | 2 | 2 | 6 | 0
A | 6 | 8 | 8 | 0
D | 3 | 11 | 15 | 0
C | 8 | 19 | 18 | 1
E | 9 | 28 | 23 | 5
 | 28 | 68 |  | 6
EDD: Sequence B-A-D-C-E

## Slide 11: Sequencing Example
Job Work
Job (Processing) Flow Job Due Job Sequence Time Time Date Lateness
B 2 2 6 0
A 6 8 8 0
D 3 11 15 0
C 8 19 18 1
E 9 28 23 5
28 68 6
EDD: Sequence B-A-D-C-E
Average completion time = Sum of total flow time = 68/5 = 13.6 days
Number of jobs
jobs in the system
Total job work time
Utilization = Sum of total flow time = 28/68 = 41.2%
Average number of = Sum of total flow time = 68/28 = 2.43 jobs
Total job work time
Average job lateness =
= 6/5 = 1.2 days
Total late days Number of jobs

## Slide 12: Sequencing Example
LPT: Sequence E-C-A-D-B
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
E | 9 | 9 | 23 | 0
C | 8 | 17 | 18 | 0
A | 6 | 23 | 8 | 15
D | 3 | 26 | 15 | 11
B | 2 | 28 | 6 | 22
 | 28 | 113 |  | 48

## Slide 13: Sequencing Example
LPT: Sequence E-C-A-D-B
Average completion time =
= 103/5 = 20.6 days
Utilization = 28/103 = 27.2%
Average number of jobs in the system = 103/28 = 3.68 jobs
Average lateness = 48/5 = 9.6 days

## Slide 14: Sequencing Example
Rule | Average Completion Time (Days) | Utilization (%) | Average Number of Jobs in System | Average Lateness (Days)
FCFS | 15.4 | 36.4 | 2.75 | 2.2
SPT | 13.0 | 43.1 | 2.32 | 1.8
EDD | 13.6 | 41.2 | 2.43 | 1.2
LPT | 20.6 | 27.2 | 3.68 | 9.6
Summary of Rules

## Slide 15: Comparison of Sequencing Rules
No one sequencing rule excels on all criteria
SPT does well on minimizing flow time and number of jobs in the system
But SPT moves long jobs to the end which may result
in dissatisfied customers
FCFS does not do especially well (or poorly) on any criteria but is perceived
as fair by customers
EDD minimizes lateness

## Slide 16: Critical Ratio (CR)
Critical ratio is an index number found by dividing the time remaining until the due date by the work time remaining on the job
Jobs with low critical ratios are scheduled ahead of jobs with higher critical ratios
Performs well on average job lateness criteria
CR =
=
Due date -Today’s date
Processing time
Time remaining
Processing time

## Slide 17: Critical Ratio Example
Job | Job Work Time | Due Date | CR
A | 6 | 8 | (8-0)/6 =1.33(lowest)
B | 2 | 6 | (6-0)/2=3
C | 8 | 18 | (18-0)/8=2.25
D | 3 | 15 | (15-0)/3=5
E | 9 | 23 | (23-0)/9 = 2.56
So, at day 6 , A is completed. The new Critical Ratios are:

## Slide 18: Critical Ratio Example
Job | Job Work Time | Due Date | CR
B | 2 | 6 | (6-6)/2=0 (lowest)
C | 8 | 18 | (18-6)/8=1.5
D | 3 | 15 | (15-6)/3=3
E | 9 | 23 | (23-6)/9=1.89
So, at day 8, B is completed. New Critical Ratios
are:

## Slide 19: Critical Ratio Example
Job | Job Work Time | Due Date | CR
C | 8 | 18 | (18-8)/8=1.25 (lowest)
D | 3 | 15 | (15-8)/3=2.33
E | 9 | 23 | (23-8)/9=1.67
So, at day 16, C is completed. New Critical Ratios are:
Job | Job Work Time | Due Date | CR
D | 3 | 15 | (15-16)/3 = -0.33 (lowest)
E | 9 | 23 | (23-16)/9= 0.78

## Slide 20: Critical Ratio Example
So the sequence is A-B-C-D-E
Job Sequence | Job Work (Processing) Time | Flow Time | Job Due Date | Job Lateness
A | 6 | 6 | 8 | 0
B | 2 | 8 | 6 | 2
C | 8 | 16 | 18 | 0
D | 3 | 19 | 15 | 4
E | 9 | 28 | 23 | 5
 | 28 | 77 |  | 11

## Slide 21: Critical Ratio Example
Average completion time = 77/5 = 15.4 days Utilization = 28/77 = 36.4%
Average number of jobs in the system = 77/28 = 2.75
jobs
Average lateness = 11/5 = 2.2 days

## Slide 22: Sequencing N Jobs on Two Machines: Johnson’s Rule
Works with two or more jobs that pass through the same two machines or work centers
Minimizes total production time and idle time

## Slide 23: Johnson’s Rule
List all jobs and times for each work center
Choose the job with the shortest activity time. If that time is in the first work center, schedule the job first. If it is in the second work center, schedule the job last.
Once a job is scheduled, it is eliminated from the list
Repeat steps 2 and 3 working toward the center of the sequence

## Slide 24: Johnson’s Rule Example
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 25: Johnson’s Rule Example
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
A
B
A

## Slide 26: Johnson’s Rule Example
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
A
B
A
B
C
C
E D

## Slide 27: Johnson’s Rule Example
B E D C A
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12

## Slide 28: Johnson’s Rule Example
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Time 0
3
10
20
28 33
35
B
A
C
D
E
WC
1
WC 2
B E D C A
B
E
E
D
C
A

## Slide 29: Johnson’s Rule Example
Job | Work Center 1 (Drill Press) | Work Center 2 (Lathe)
A | 5 | 2
B | 3 | 6
C | 8 | 4
D | 10 | 7
E | 7 | 12
Time 0
3
10
20
28 33
Time 0
1 3 5 7 9 10 11 12 13 17 19 21 22 2325 27 29 31 33 35
B
A
C
D
E
B
A
C
D
E
WC
1
WC 2
B
E
D
C
A
B E D C A

## Slide 30: Practice Yourself
JOB | Work center(1) | Work center(2)
A | 7 | 2
B | 9 | 4
C | 3 | 5
D | 1 | 2
E | 5 | 8

## Slide 31: Gant Chart
This is also known as “Gant Chart” or time phrase chart.
Note: When you will compare the data always compare it with all the data. If there are 10 processing time of 2 work centers for choosing the sequence u need to consider all the jobs.